## Slide 1: Lab 6: Matrix Multiplication Circuit Design
National Chiao Tung University
Chun-Jen Tsai
10/30/2015

## Slide 2: Lab 6: Matrix Multiplication
In this lab, you will design a circuit to do 4x4 matrix multiplications
  Read two 4x4 matrices from the UART port
  Each matrix has 16 unsigned 8-bit elements
  When the west button is pressed, it triggers the multiplication of the two matrices
  The output matrix has 16 unsigned 18-bit elements
  Print the output matrix through the UART to a terminal window
You will demo the design to your TA during the lab hours on 11/16

## Slide 3: Design Constraint of Lab6
You can use no more than 16 multipliers to implement your system
  Spartan-3E XC3S500E FPGA has 20 18-bit multipliers
Your grade will be based on correctness, logic usage, performance, and your skill of coding

## Slide 4: Suggested Datapath of A44  b41
a00
a10
a20
a30
a01
a11
a21
a31
a03
a13
a23
a33

b0

b1

b3
+
+
0
1
2
3
0
1
2
3
0
1
2
3
a02
a12
a22
a32
0
1
2
3
b2

+
one output per clock cycle after initial delay
2
m1
m2
m3
m4
You may not need these registers.
Row select

## Slide 5: Design a FSM to Re-use the Datapath
You can design a FSM to control the row select signal so that the A44  b41 datapath can finish computation in 4+1 clock cycles
For A44  B44, you can duplicate the matrix-vector multiplication module four times, so, supposedly, 44 matrix multiplication can be computed in five clock cycles

## Slide 6: Input-Output of the System
A binary data file of the two matrices will be send from the TeraTerm window to the FPGA via the UART port
  The binary data file is of 32 bytes
You must design a module to convert the resulting matrix into ASCII text and print it to the TeraTerm window
  Each number (18-bit) of the matrix is displayed with 5 hex digits, for example, 7C4 should be printed as 007C4
  There must be a space character between two numbers
  Print a CR/LF pattern (i.e., 0D 0A) after each row of numbers